TENDER No: - F.1 (ICSIL)/HW /01/2012-13/ Tender No. 212 dated 09/10/2012

Sealed quotations from Original Equipment Manufacturers (OEM) / Authorized Business Partners of OEMs of various make are invited as per the make / specifications given in the tender document for supply, installation and commissioning at Delhi Transco Limited located in Delhi. The tender time lines are as under.

- Last date of submission of Sealed Quotations   : - On or before 16 Oct 2012 by 01:00 P.M.  in the office of Dy. General Manager, Ist Floor,  ICSIL ‘s office , Administrative Building , Okhla – Phase- III ,Behind Modi Mill , New Delhi- 110020

- Date and Time of opening of Sealed Quotations: - 16 Oct 2012 by 02:00 P.M.

Interested bidders may quote the rates as per the format given in the Tender document for the following items:-

Items:-

| S.No. | Material Name | Detailed Description | Quantity | Unit Rate in Rs |
| --- | --- | --- | --- | --- |
| 1 | Switch | Managed Layer 2 fibre to Ethernet switch, 61850-3 compliant Ethernet switch. Technical Specifications :- The switch shall be of industrial grade type designed for continuous operation. Switch shall have minimum 8 copper ports – RJ45 ports. Switch shall have 2 Giga-fibre ports- SFP single mode. Switch shall be 19 inch rack mountable. Switch shall support IEEE802 series for VLAN, RSTP,MSTP, Suitable for ring configuration etc. Switch shall be IEC 61850 EMC and operating conditions for Power Substations Complaints. Switch shall be IEEE 1613 Environmental Standard for Electric Power Substations complaint. | 3 |  |

Note: - Rate should be inclusive of all taxes, duties, cess etc.

General Conditions:

RATES & TAXES-------Rates quoted must be inclusive of all taxes, duties, levies, cess, fees, service Tax Transport / Delivery /Installation Charges etc., and no increase in price shall be allowed subsequent to award of work / purchase order under any circumstances.

SERVICE TAX REGISTRATION -------- Service Tax registration is mandatory.  Please attach proof of valid Service Tax Registration Certificate.

DVAT REGISTRATION------- DVAT Registration is mandatory.  Please attach proof of valid DVAT Registration Certificate.

MAF/ AUTHORIZED PARTNER CERTIFICATE: --------The bid must be accompanied with either Manufacturer’s Authorization Form or Authorized Partner Certificate issued by OEM.

DELIVERY-----Goods shall have to be delivered within a period of 2-3 weeks time.

PAYMENT ---- Payment of 80% shall be released after delivery, installation of all items and after submission of INVOICE, DELIVERY CHALLANS, and INSTALLATION REPORTS to ICSIL duly certified by the client department subject to the condition that ICSIL has received 80% advance from client. Balance 20% shall be released on back to back basis i.e. after receipt of payment from the client.

INSPECTION----- Post delivery inspection may be carried out by ICSIL, if required.

SUPPLY-------Supply of goods shall have to be made directly to the department, on site, the detail of which shall be provided at the time of grant of work / purchase order.

Rates Quoted---- Rates quoted should not be more then rates quoted to any Govt.Deptt/PSU/ in past one year. A certificate to this effect should be submitted by the bidder.

Quantity------- quantity mentioned in tender is tentative and may vary.

ICSIL reserves the right to cancel/ terminate the tender at any stage without assigning any reason